## Slide 1: EDES 301 Prosthetic Grip Proposal
2/23/2025
Tarik Price

## Slide 2: Background Information
What is being proposed?
  I want to improve upon a previous ENGI 301 project involving the use of a prosthetic finger. Currently, the prosthetic uses a potentiometer to adjust the position of the finger. However, that does not address the forces felt whenever one grips an object. My goal is to improve upon the current design to address grip strength
  https://www.hackster.io/pkim7035/6-finger-augmentation-with-pocketbeagle-d0ea5d
What improvements / additions over existing project
  I would like to replace the potentiometer with a force sensing resistor as it provides more information on the grip strength of the prosthetic
  I would also like to expand on the single finger and add two more fingers to mimic the holding of an object. This change will require a new code to control each new finger

## Slide 3: System Block Diagram
User Input
FSR
Signal Conditioning
Analog Signal
Pocket Beagle (I2C,GPIO)
Control Signals
Servo/Motor Driver
Prosthetic
Servo Control

## Slide 4: Power Block Diagram
Power Supply (5V Battery
Pocket Beagle (5V Supply Voltage, 200 mA current
Servo/Motor Driver (5-6V Supply, 1A current)
Servo Motors (5-6V Supply, 0.5-2A current)
FSR (3.3-5V Supply, <50mA current)

## Slide 5: Components / Budget
Component | EDES301 to Buy? | Cost
SG90 Micro-Servo Motor (or Stepper Motor) | Yes/No | $13.99
Force Sensitive Resistor (or EMG sensor) | Yes | $6.75
Velcro Straps (12 “ x ½”) | Yes/No | $13.49
Elastic Fishing Line | Yes/No | $4.99
Orthodontic Elastic Rubber Band (3/16”) | Yes | $4.99